## Slide 1: Redefining the Driver's Attention Gauge in Semi-Autonomous Vehicles
Raja Hasnain Anwar*, Fatima Muhammad Anwar*, Muhammad Kumail Haider†, Alon Efrat‡, and Muhammad Taqi Raza*
*University of Massachusetts Amherst, †Meta Platforms, ‡University of Arizona
Khwarizmi
Lab
MWSiM’23
Montreal, Canada
November 1, 2023

## Slide 2
Photos licensed under CC BY-SA-NC and CC BY-NC-ND
How do you kill time in stop-and-go traffic:
Catch up on the game or stay updated with the latest news?

## Slide 3: Distracted & Deadly Driving
Distracted driving accounts for 14.4% of all fatal and 22.1% of non-fatal crashes[1].
Can semi-autonomous vehicles save us?
[1] Kara Kockelman et al. An Assessment of Autonomous Vehicles: Traffic Impacts and Infrastructure Needs—Final Report. UT Austin 2017
Photo licensed under CC BY-SA-NC and CC BY-NC-ND

## Slide 4: Semi-autonomous Vehicles: A driver’s aid or replacement?
There is a false sense of safety[2,3].
“Semi”-autonomous vehicles rely on humans for critical input.
A distracted driver takes an impulsive action.
  Often (1.5 seconds) late[4] and fatal.
[2] https://cars.usnews.com/cars-trucks/features/drivers-overestimate-self-driving-capabilities
[3] https://www.cbc.ca/news/canada/windsor/windsor-university-study-distracted-driving-1.6715465
[4] Alexander Eriksson et al. Takeover Time in Highly Automated Vehicles: Noncritical Transitions to and From Manual Control. Human Factors 2017
Photo licensed under CC BY-SA-NC and CC BY-NC-ND

## Slide 5: Existing Approaches to Alert the Driver
[5] https://www.theverge.com/2020/3/3/21162310/2021-mercedes-benz-e-class-capacitive-wheel-geneva-motor-show
Steering wheel pressure sensors (Mecedes-Benz[5])
Photos licensed under CC BY-SA-NC and CC BY-NC-ND
Head and eyes tracking (Kubler et al., 2021)
Facial expressions
(Dua et al., 2019)
Wearable devices
(Wang et al., 2021)
Average human attention span is about 8 seconds!

## Slide 6: Redefining the Driver’s Attention
Drivers do not require constant attention
Vehicle processes different events differently
Not all alerts have the same priority
Reckless Driving
Sudden Stop

## Slide 7: Event-based Attention
Every traffic scenario warrants a unique response from the driver.
  Criticality and timeliness
  Recall reckless driving vs sudden stop
Every traffic scenario engages a unique set of hardware resources.
  Sensors: RGB, Depth, Radar, Lidar[6]
Defining driver’s attention as a function of critical external events.
  Estimating criticality and timeliness from resource usage.
[6] Self-driving Safety Report. General Motors 2018
General Motors
Scenario | Sensors
Jaywalking | RGB, Depth, Radar, Lidar
Reckless Driving | RGB, Radar
Sudden Lane Change | RGB, Depth, Radar
Sudden Stop | RGB, Lidar
Poor Weather | Lidar, Radar
Road Bump | RGB, Depth
Notes: under the poor weather condition, the semi-autonomous vehicle tries to ensure that the vehicle should not depart from its lane; whereas, the sudden appearance of a foreign object (e.g., a pedestrian jaywalking or an animal crossing the road), the vehicle applies the brakes and/or changes its course safely. These are critical scenarios that mandate that the driver should be attentive in a timely manner. However, two critical events cannot be of the same importance. For example, avoiding a foreign object is more critical than steering the vehicle within its lane on a bumpy road. Therefore, it is important to alert the driver according to the criticality of the event.

## Slide 8: Events as Unique Processes
Separate Simulations
Joint Simulations
)

## Slide 9: Modeling Traffic Events into Attention Feedback
We analyze the vehicle ECU (controller) processing patterns.
  is the measure of event over time interval .
Traffic events follow Markovian process:
  The driver’s action is only dependent on the present traffic state (i.e., sudden stop).
Resource usage follows Poisson process where:
  𝜆 is the rate of the system usage (i.e., peaks) for the event per unit of time.
  𝑡 is the length of the time interval.
Markov-Poisson model: an event triggers a resource usage spike depending on the criticality of the event.
Event
Response
Jay Walking

## Slide 10: Experimental Setup
Carla simulator (0.9.11) running on a general-purpose PC.
  2.8 GHz processor
  32 GB Memory
ECU implemented on an NVIDIA Jetson Xavier AGX.
Workload:
  NVIDIA Autopilot[7] for RGB and Depth
  Cylinder3D[8] for Lidar
  RODNet[9] for Radar
[7] Bojarski et al. End to End Learning for Self-Driving Cars. NVIDIA 2016
[8] Zhu et al. Cylindrical and asymmetrical 3d convolution networks for lidar segmentation. CVPR 2021
[9] Wang et al. Rodnet: Radar object detection using cross-modal supervision. WACV 2021

## Slide 11: Evaluation
Timeliness of the Alert
Likelihood Estimation of Critical Event Arrival
Up to 75x faster.
The theoretical probability of an event is an average of all estimated probabilities.
Notes: The high similarity between observed and estimated probabilities indicates that (a) our model correctly selects the appropriate 𝜆 using the present state as prior, and (b) it estimates the likelihood of occurrence of a critical traffic scenario with high accuracy and confidence.

## Slide 12: Thank you for your attention!
Contact:
Raja Hasnain Anwar (ranwar@umass.edu) KhwarizmiLab.github.io
Conclusion
Existing driver’s attention-gauging methods are ineffective.
We propose a situation-aware driver’s attention gauge and alert mechanism.
Only engage the driver when safety-critical situation arises.
Estimation of timeliness and criticality of events using resource utilization spikes.
Future Work
Alerts sharing across vehicles.
VANET integration.